EPIC: A new generation of architectures  beyond RISC

Presentation at UC Berkeley

by

Mike Schlansker
Hewlett-Packard Laboratories
March 3, 1999

The uniprocessor design problem:

o	How to provide ever increasing performance for existing applications without re-writing them?

o	Modest speedups (e.g.  2´) are critical!

o	How to exploit expanding VLSI circuit area?

o	Substantial area should be devoted to Instruction-Level Parallelism (ILP)

m	How to issue many operations per cycle?  (4-16)

m	How to tolerate long pipelined latency?  (1-50)

m	How to cope with a large number of operations in flight?  (10’s to 100’s)

EPIC: a paradigm shift

o	RISC solution

m	Based on sequential execution semantics

m	Compiler’s role is limited by the instruction set architecture

m	Superscalar hardware identifies and exploits parallelism

o	EPIC solution – (the evolution of VLIW)

m	Based on parallel execution semantics

m	EPIC ISA enhancements support static parallelization

m	Compiler takes greater responsibility for exploiting parallelism

m	Compiler / hardware collaboration often resembles superscalar

Why pursue new architectures?

o	Disadvantages of continuing a pure out-of-order superscalar approach

m	Out-of-order execution is complex for high ILP

- expensive in real estate

- difficult to debug & verify

m	No existence proof at high levels of ILP

o	Advantages of pursuing EPIC architectures

m	Make wide issue & deep latency less expensive in hardware

m	Allow processor parallelism to scale with additional VLSI density

EPIC philosophy

o	Architect the processor to do well with in-order execution

m	Enhance the ISA to allow static parallelization

m	Use compiler technology to parallelize program

o	However, a purely static VLIW is not appropriate for general-purpose use

The fusion of VLIW and superscalar techniques

o	Superscalars need improved support for static parallelization

m	Static scheduling

m	Limited support for predicated execution

o	VLIWs need improved support for dynamic parallelization

m	Caches introduce dynamically changing memory latency

m	Compatibility: issue width and latency may change with new hardware

m	Application requirements - e.g. object oriented programming with dynamic binding

o	EPIC processors exhibit features derived from both

m	Interlock & out-of-order execution hardware are compatible with EPIC    (but not required!)

m	EPIC processors can use dynamic translation to parallelize in software

Many EPIC features are taken from VLIWs

Minisupercomputer products stimulated VLIW research (FPS, Multiflow, Cydrome)

m	Minisupercomputers were specialized, costly, and short-lived

m	Traditional VLIWs not suited to general purpose computing

m	VLIW resurgence in single chip DSP & media processors

Minisupercomputers exaggerated forward-looking challenges:

m	High-speed clock

m	Long latency

m	Wide issue

m	Large number of architected registers

m	Compile-time scheduling to exploit exotic amounts of parallelism

EPIC exploits many VLIW techniques

VLIW compilers must create

an efficient ILP record of execution

Trace scheduling (Fisher at Multiflow)

Use static program statistics to identify traces

Schedule code across basic blocks to maximize on-trace performance

Treats arbitrary scalar programs

Speculative code motion

Basic blocks are short & sufficient ILP requires motion across blocks

Speculation reduces height of program schedule by changing operation’s execution condition

Exceptions must be ignored – dismissable load (Multiflow)

Modulo scheduling (Cydrome)

Near optimal performance for innermost-loops

More flexible than vector - treats recurrences and while loops

Specialized branch and rotating registers eliminate code replication (Rau)

Predicated execution of if-converted code

Efficient treatment of many unbiased conditionals

Allow code motion without changing operation’s execution condition

Predicated execution: hardware support

| compare operation | predicated operation |
| --- | --- |

VLIW architectural features prior to 1989

Wide issue (MultiOp)

Exposed latency

Large number of architected registers

Dismissable loads

Rotating registers & specialized branches to support software pipelining

Predicated execution

Execution of multiple prioritized branches per instruction (Multiflow)

Shortcomings of first generation of VLIWs

Expensive multi-chip implementations

o	No data cache

Poor "scalar" performance

No strategy for object code compatibility

EPIC design challenges

o	Develop architectures applicable to general-purpose computing

m	Find substantial parallelism in “difficult to parallelize” scalar programs

m	Provide compatibility across hardware generations

m	Support emerging applications (e.g. multimedia)

o	Compiler must find or create sufficient ILP

o	Combine the best attributes of VLIW & superscalar RISC                           (incorporated best concepts from all available sources)

o	Scale architectures for modern single-chip implementation

HPL PlayDoh: a testbed for EPIC architectures

o	PlayDoh - HP Laboratories virtual processor for ILP research

o	Virtual platform provides compiler & simulator for  PlayDoh ISA

o	Publicly available for external research

o	Remainder of talk highlights EPIC features found in PlayDoh

The second generation: some key EPIC features

o	Generational compatibility

o	Improved support for control speculation

o	Programmatic control of the cache hierarchy

o	Data speculation

o	Improved support for predication

o	Unbundled & concurrent branches

Latency compatibility

o	Schedule code using actual hardware latencies of target processor

o	Compile with “less than or equals semantics”  to allow early arrival

o	Two approaches use hardware for late operand arrival:

m	Use exposed latency semantics & “latency stalling” (tardy operand stalls)

m	Use unit latency semantics & interlocks (tardy operand stalls if used)

Control speculation and exception reporting

o	Need: accurate error reporting

o	Need: ability to handle exceptions

Deferred exception handling

o	Speculative & non-speculative opcodes, operand tags, propagation rules   [Cydrome; Ebcioglu; Mahlke, et al.]

o	 Software responsible for error isolation and recovery

Problems involving data caches

Absence of a data cache increases critical path length (especially for scalar code)

Presence of data cache degrades performance with poor data locality (cache thrashing and cache trashing)

Non-deterministic latencies are a problem for static scheduling

m	Assuming cache hits results in total dead time when the cache misses

m	Assuming cache misses results in pessimistic schedules

EPIC objectives: enhance run-time determinism using compile-time data cache management

Programmatic data cache management

| bypass & latency specifying loads | pretouch and prefetch |
| --- | --- |

Compiler directs motion of data through cache hierarchy

[Convex C-1; Intel i860; Chi & Dietz 1989]

Memory dependences and static scheduling

“May” dependences on the critical path

Original Code

*a=*b

*c=*d

*e=*f

Schedule height = 12

Memory latency =10 ?

o	Cache alleviates problem by reducing latency - but may cause pollution

Data speculation

| Schedule height = 9 |  |
| --- | --- |

Schedule height = 5

Dependence graph

with 2-cycle cache latency

Dependence graph

with data speculation

o	Data speculation: Stores in lds-ldv window checked in hardware [Chen 93]

o	Does not require cache and cache pollution

Improved architecture for predicates

PlayDoh code for C conditional    “r=(a<b)?a:b”

is written:

p1,p2=cmpp.w.<.UN.UC(a, b)if p

r = a if p1

r = b if p2

Predicate input

Compare

| result | UN | UC |
| --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 0 |

o	Compound & two-target compare minimizes latency & op count

o	Unconditional actions UN and UC support simple & nested conditionals

Unconditional compares do not support general  if-conversion

A if p

p1, p2, p3  = ...

B if p1;

p4 = cmpp.w.<.UC(a, b)

C if p2;

p4 = cmpp.w.<.UC(c, d)

D if p3

p4 = cmpp.w.>.UN(e, f)

E if p4

Wrong code

o	For unstructured code:

m	A merge block has multiple operations that set its predicate

m	Need to compute:  p4 = OR(  p1!(a < b) ,   p2!(c < d) ,   p3(e > f))

m	Results are incorrect if unconditional (UN, UC) compares are used

Solution "Wired-or compares"

Allows multiple writes per cycle

If they write identical values, the result is well-defined

| Ops can be issued in any order or concurrently |  |
| --- | --- |

Predicate input

Compare

| result | ON | OC |
| --- | --- | --- |
| 0 | 0 | -- | -- |
| 0 | 1 | -- | -- |
| 1 | 0 | -- | 1 |
| 1 | 1 | 1 | -- |

o	OR class compares use target action modifiers ON and OC

Wired or compares (cont)

o	An n-term wired or is calculated with:

m	a single clear

m	n unary or operations

The following sequence computes predicate p4 as defined above:

p4 = 0

p4 = cmpp.w.<.OC(a, b)  if p1

p4 = cmpp.w.<.OC(c, d)  if p2

p4 = cmpp.w.>.ON(e, f)  if p3

Chains of predicate computations inhibit ILP

Linked compare computation

If-converted code:

...

p2 = cmpp.w.=.UN(t, 'M') if T

p3 = cmpp.w.>.UC(r, 0)   if p2

p5 = cmpp.w.=.UN(r, 0)   if p3

s = 0.8 * s if p5

...

Need to compute:  p5=AND(  (r=0),   !(r>0),   (t=‘M’)  )

"Wired and" works like "wired or" for fast evaluation of n-way AND

Conventional conditional branch operation

o	 Problem: compound branch components are statically co-located

Unbundled conditional branch sequence

[Schorr 1971, Young & Goodman 1984]

Concurrent branching

using Fully-Resolved Predicates (FRPs)

| Branch dependences | Unordered branches with FRPs |
| --- | --- |

Summary: key EPIC  features

o	Motivations

m	To avoid out-of-order execution

m	To enhance ILP on "sequential" computations

m	To address the cache miss penalty

o	Some EPIC architectural features

m	Compatibility strategy for evolving implementation parallelism

m	Control speculative opcodes with exception tags & propagation

m	Programmatic control of cache hierarchy

m	Data speculative loads

m	Improved predication (two-target & unordered compares)

m	"Unbundled" branch architecture

m	Concurrent branching

Compiling for EPIC?

o	Complex portfolio of architectural innovations

o	New optimizations reduce path length rather than operation count

o	New compiler techniques will evolve for EPIC architectures

m	Expose ILP - analyze code to maximize available parallelism

m	Enhance ILP - transform code to increase available parallelism

m	Exploit ILP - map code onto available hardware to maximize efficiency

m	Manage the cache hierarchy

m	Extend traditional analyses and optimizations for predicated code

m	Object code translation

Control CPR - example compiler optimization

| Superblock CFG | Insert fall-through branch & lookahead compares | Branches & compares move off-trace |
| --- | --- | --- |

Summary

o	Uniprocessor performance remains a key product objective

o	EPIC processors:

m	Take advantage of evolving VLSI density

m	Exploit additional instruction-level parallelism using enhanced ISA

m	Shift responsibility for exploiting parallelism from hardware to software

m	Are designed to address general computing needs

o	Performance improves as EPIC compilers mine more ILP over a wider range of applications